## Slide 1: IDETC 2024 Hackathon
Missing Frame Detection in Additive Manufacturing
Jiacheng Sun
August 25, 2024

## Slide 2: Background and Problem Statement
The Additive Manufacturing Metrology Testbed (AMMT) system may lose in-situ images during the manufacturing process due to camera triggers not synchronizing with the machine’s operations.
The challenge is to accurately locate the missing frames in the sequence to ensure data continuity and reliability.

## Slide 3: Background and Problem Statement
Part 1: The missing frames have been retrieved, and the task is to correctly place them back into the sequence.
Part 2: The missing frames are permanently lost, and the task is to determine where they were lost based on the remaining sequence.
Objective: Develop a method that is accurate, robust, and efficient in detecting and placing missing frames within the sequence.

## Slide 4: Methodology: Similarity Calculations
Problem Understanding
  For both parts of the challenge, identifying the exact position of missing frames relies heavily on understanding the temporal sequence and changes between frames.

## Slide 5: Methodology: Similarity Calculations
Similarity Calculation Techniques
  Mean Squared Error (MSE)
    Captures the global pixel-level differences between consecutive frames. Lower MSE indicates higher similarity.
  Sobel Edge Detection
    Highlights the edges within frames, capturing significant changes that might indicate missing frames. Differences in edge maps between consecutive frames were computed and analyzed.

## Slide 6: Methodology: Calculation and Selection
Part 1
  Missing frames were compared against the surrounding frames using MSE and edge detection.
  The goal was to place the frame where it minimized discrepancies in these metrics.

## Slide 7: Methodology: Calculation and Selection
Part 1
  Edge Detection
    Canny Edge Detection was used to extract the contours of the bright spot, reducing the influence of background noise.
Formula 1 Canny Edge Detection

## Slide 8: Methodology: Calculation and Selection
Part 1
  MSE Calculation
    To compare the missing frames with the given frames, the MSE between their edge-detected versions was calculated.
Formula 2 MSE Calculation
where I and J are the two images being compared, and N is the total number of pixels in the images.

## Slide 9: Methodology: Calculation and Selection
Part 1
  Best Matching
    For each missing image, its MSE was calculated against every given image, and the position with the smallest MSE was selected as the best match.
    These matches were visualized for manual verification.
Fig. 1 One of the results of the best matching

## Slide 10: Methodology: Calculation and Selection
Part 2
  Without the missing frames, differences between consecutive frames were used to identify potential gaps.
  Combined the results from the similarity calculations to generate a composite score.

## Slide 11: Methodology: Calculation and Selection
Part 2
  Sobel Edge Detection
    Sobel Edge Detection is used to extract edge information from the images and calculate changes between consecutive frames.
Formula 3 Sobel Edge Detection
where I(i,j) represents the pixel value of the image, and Kx and Ky are the kernels of the Sobel operator used for edge detection in the x and y directions.

## Slide 12: Methodology: Calculation and Selection
Part 2
  Difference Calculation
    For each frame, the differences between it and the previous frame and the next frame are calculated.
Formula 4 Difference Calculation
where I and J are the edge-detected images, and N is the total number of pixels in the images.

## Slide 13: Methodology: Calculation and Selection
Part 2
  Total Score
    For each frame, the total score is calculated by summing the differences with its neighboring frames. A higher score indicates a significant change, suggesting a missing frame.
Formula 5 Total Score
where Ii is the current frame, Ii−1 is the previous frame, and Ii+1 is the next frame.

## Slide 14: Methodology: Calculation and Selection
Part 2
  Selection Process
    For each frame, the difference score was calculated and sorted to identify the most likely positions of missing frames.
    For Part 2, the top 50 positions with the highest scores were selected as potential missing frame locations.
Fig. 2 One of the results of the total score

## Slide 15: Conclusion and Future Work
Flexibility
  The methodology was adaptable to different data scenarios, including variations in image structure and content.

## Slide 16: Conclusion and Future Work
Weaknesses
  Processing Time: The combination of multiple similarity metrics increased computational complexity, which could impact real-time applications.
  Sensitivity to Noise: The methodology might be sensitive to image noise, particularly in edge detection, leading to potential false positives.

## Slide 17: Conclusion and Future Work
Future Work
  Explore more efficient algorithms or dimensionality reduction techniques to enhance processing speed.
  Integrate noise reduction techniques to improve the robustness of edge detection and overall similarity calculations.
  Consider applying machine learning models to learn and predict missing frames based on patterns from labeled data.